## Slide 1
DEPARTMENT OF ECE · MACHINE LEARNING · A.Y. 2026-27
Temporal Fusion Transformer-Based Multi-KPI Forecasting for Proactive Open RAN Control
Project Review Presentation
Presented by
Chandra Nikhilesh | 2520040091
Sujeeth Reddy | 2520040025
Sai Charan | 2520040021
Under the guidance of
<Guide Name>
<Designation, Department>

## Slide 2
Problem Statement
TFT Multi-KPI Forecasting for Proactive Open RAN Control | 2 / 10
Open RAN makes the radio network open and programmable through RAN Intelligent Controllers (RICs). Network KPIs still change constantly with traffic, mobility and radio conditions.
Highly dynamic KPIs
Throughput, latency, packet loss, PRB utilisation and active users vary sharply over time and between cells.
Reactive control is late
Today’s control acts only after congestion or QoS degradation is detected, so users are already affected.
Isolated KPI models
Forecasting one KPI at a time ignores the strong coupling between load, resources and QoS.
Goal: Jointly forecast multiple KPIs several steps ahead with a Temporal Fusion Transformer, so the RIC can act before degradation happens.

## Slide 3
Methodology: Temporal Fusion Transformer
TFT Multi-KPI Forecasting for Proactive Open RAN Control | 3 / 10
Static
Cell ID embedding
Past observed
5 KPIs, last 12 h
Known future
Time of day, day of week, weekend
Variable Selection
Networks
Learn which inputs matter at each step
LSTM Encoder–
Decoder
Captures local temporal patterns
Multi-Head
Attention
Long-range dependencies, interpretable weights
Quantile
Output
P10 / P50 / P90 for all 5 KPIs
Gated Residual Networks (GRN) and gating layers wrap every block and suppress unneeded components.
Why TFT?
Multi-horizon, multi-variate forecasts in a single model
Uses known future inputs (calendar/time) alongside past KPIs
Interpretable: variable importance and attention show why a forecast was made
Quantile outputs give uncertainty bands for risk-aware control

## Slide 4
Algorithm: Forecast-Driven Proactive Control
TFT Multi-KPI Forecasting for Proactive Open RAN Control | 4 / 10
1
Input
Sliding window of the last 48 steps (12 h, 15-min interval) of 5 KPIs plus time covariates for each cell
2
Normalise
Z-score scaling using training-set statistics only
3
Forecast
TFT predicts the next 12 steps (3 h) for all KPIs at quantiles q = 0.1, 0.5, 0.9
4
Train
Minimise quantile (pinball) loss L = Σ max(q·e, (q−1)·e), where e = y − ŷ
5
Decide
If predicted P90 PRB utilisation or latency crosses a threshold → raise an early alert
6
Act
RIC xApp adjusts PRB allocation, load balancing or handover policy ahead of time

## Slide 5
Project Workflow & Implementation
TFT Multi-KPI Forecasting for Proactive Open RAN Control | 5 / 10
Data collection / simulation
Per-cell KPI time series
Pre-processing
Cleaning, scaling, time features
Window generation
12 h input → 3 h output
TFT training
Quantile loss, early stopping
Multi-step forecasting
5 KPIs with P10/P50/P90
Proactive control
Alerts and RIC policy actions
Where it runs in O-RAN
Non-RT RIC (rApp)
Offline training and periodic re-training on KPI history (> 1 s loop)
Near-RT RIC (xApp)
Online inference and control actions (10 ms – 1 s loop)
E2 nodes (O-CU / O-DU)
Report KPIs over E2 and apply the chosen policy
Tools: Python 3, PyTorch, NumPy / pandas, scikit-learn, Matplotlib, Google Colab / Jupyter

## Slide 6
Simulation Setup
TFT Multi-KPI Forecasting for Proactive Open RAN Control | 6 / 10
12
O-RAN cells
28
days @ 15-min
5
KPIs forecast
48 → 12
steps in → out
Dataset | Simulated per-cell KPIs: daily and weekly traffic cycles, random traffic bursts, congestion-coupled latency and packet loss
KPIs | Throughput (Mbps), latency (ms), packet loss (%), PRB utilisation (%), active UEs
Split | Chronological 70 / 15 / 15 % → train / validation / test (4,716 test windows)
TFT model | Hidden size 48, 4 attention heads, ≈ 313 k parameters, Adam, 20 epochs, best-validation checkpoint
Baselines | Persistence (last value), seasonal naive (same time yesterday), 2-layer LSTM
Metrics | MAE, RMSE, MAPE per KPI; prediction-interval coverage

## Slide 7
Results: Forecast Accuracy
TFT Multi-KPI Forecasting for Proactive Open RAN Control | 7 / 10
Chart: Mean normalised MAE, test set (lower is better)
| Seasonal naive | Persistence | LSTM | TFT (ours)
Normalised MAE | 0.745 | 0.708 | 0.499 | 0.477
MAE per KPI (3-h horizon average)
KPI | TFT | LSTM | Persist.
Throughput (Mbps) | 16.36 | 17.47 | 25.56
Latency (ms) | 0.91 | 0.94 | 1.34
Packet loss (%) | 0.024 | 0.025 | 0.034
PRB util. (%) | 7.98 | 8.51 | 12.11
Active UEs | 5.56 | 5.97 | 8.76
33 % lower error than persistence and 4.5 % lower than LSTM. TFT gives the lowest MAE on every KPI, and RMSE follows the same trend.

## Slide 8
Results: Forecast Behaviour & Interpretability
TFT Multi-KPI Forecasting for Proactive Open RAN Control | 8 / 10
PRB utilisation, 1-h-ahead TFT forecast vs actual on unseen test data
Chart: Error vs horizon (hours ahead)
| 1 | 2 | 3
TFT | 0.372 | 0.408 | 0.436 | 0.458 | 0.474 | 0.488 | 0.499 | 0.506 | 0.513 | 0.518 | 0.522 | 0.526
LSTM | 0.369 | 0.414 | 0.447 | 0.473 | 0.494 | 0.509 | 0.525 | 0.536 | 0.544 | 0.554 | 0.558 | 0.565
Persistence | 0.449 | 0.51 | 0.565 | 0.611 | 0.657 | 0.704 | 0.743 | 0.782 | 0.822 | 0.854 | 0.886 | 0.915
79.6 %
of actual values fall inside the P10–P90 band (target 80 %), so the uncertainty is well calibrated
−42 %
error vs persistence at the 3-h horizon; TFT degrades slowest as the horizon grows
Time of day
is the most important input (39 % VSN weight), followed by throughput (13 %) and PRB (11 %)

## Slide 9
Current Progress & Remaining Work
TFT Multi-KPI Forecasting for Proactive Open RAN Control | 9 / 10
Completed
Literature review on O-RAN, RIC and time-series forecasting
Multi-KPI O-RAN traffic simulator built
Pre-processing and sliding-window pipeline
TFT implemented and trained with quantile loss
Baselines (persistence, seasonal naive, LSTM) compared
Accuracy, horizon and interpretability analysis
Remaining
Validate on a real / testbed O-RAN KPI dataset
Hyperparameter tuning and ablation (without attention / VSN)
Build the proactive control module (threshold alerts to PRB and load-balancing actions)
Evaluate early-warning lead time and precision on congestion events
Package as an xApp prototype and write the final report

## Slide 10
Conclusion
A single TFT model forecasts 5 O-RAN KPIs up to 3 h ahead, with calibrated uncertainty.
On simulated data it beats persistence by 33 % and LSTM by 4.5 %, with the widest gain at longer horizons.
Interpretable outputs show why a forecast was made, which builds operator trust.
Next: real-data validation and closing the loop with RIC control actions.
Thank You
Questions & discussion